NOTE: This page was found in the Archive.org Web Server. Please note that it was not created by AKM, it was created by Elmer Boggs and posted to LS1.com. LS1.com has removed this very useful page from their web site, but in an effort to preserve the knowledge, I have resurrected it from the archives. Props to Elmer for making this page.

| Circuit Number C1 (Red) | This table contains all of the 1998 Pin connections, Wire colors, and Functions of Connector C1 (Red). There are 80 pins on this connector |
| --- | --- |

| Pin | Wire Color | Function |
| --- | --- | --- |
| 1 |  | Not Used |
| 2 |  | Not Used |
| 3 | WHT | EVAP Canister Vent Solenoid Valve |
| 4 | BRN/WHT | Camshaft Position Sensor |
| 5 |  | Not Used |
| 6 |  | Not Used |
| 7 | YEL | VSS Signal return |
| 8 |  | Not used |
| 9 | PNK/BLK | Injector #3 Control |
| 10 |  | Not Used |
| 11 | DK BLU | VTD Fuel Enable |
| 12 | LT BLU/BLK | Injector #4 Control |
| 13 | RED/WHT | Ignition #2 Control |
| 14 | DK GRN | A/C Status |
| 15 | BLK/WHT | Injector #5 Control |
| 16 |  | Not used |
| 17 |  | Not used |
| 18 | YEL/BLK | Injector #6 Control |
| 19 |  | Not used |
| 20 |  | Not used |
| 21 | PPL | IAT Sensor Ground |
| 22 | DK BLU | Transmission Range Signal B |
| 23 | LT GRN/BLK | Injector #2 Control |
| 24 | BLK/WHT | Sensor Ground Jumper |
| 25 | PNK | Transmission Range Signal A |
| 26 |  | Not used |
| 27 | RED/BLK | Injector #7 Control |
| 28 |  | Not used |
| 29 |  | Not used |
| 30 | GRY/BLK | Spark Retard Signal |
| 31 | DK BLU/WHT | Injector #8 Control |
| 32 | ORN/BLK | PNP Switch Signal |
| 33 | BLK | Injector #1 Control |
| 34 | GRY or WHT | Skip Shift Solenoid (M6), or 3-2 Shift Solenoid (A/T) |
| 35 | LT GRN | 1-2 Shift Solenoid |
| 36 | DK BLU | Fuel Gauge Output Control |
| 37 | BRN/WHT | MIL Control |
| 38 |  | Not used |
| 39 | DK GRN/WHT | A/C Clutch Relay Control |
| 40 | WHT or YEL/BLK | Skip Shift Lamp Control (M/T) or 2-3 Shift Solenoid (A/T) |

Elmer Boggs	Eboggs_jkvl	1/22/2001

Continued on next page

| Circuit Number C1 (Red) | Table continued. |
| --- | --- |

| Pin | Wire Color | Function |
| --- | --- | --- |
| 41 | BRN/WHT | Low Oil Level Indicator Lamp Control |
| 42 | LT/GRN | Reverse Inhibit Solenoid Control |
| 43 | DK/GRN | Cooling Fan relay #1 Control |
| 44 | YEL | Crankshaft Position Sensor Input |
| 45 | DK GRN/WHT | EVAP Canister Purge Valve Control |
| 46 |  | Not Used |
| 47 | DK GRN/WHT | A/C Request Signal |
| 48 | YEL | MAF Signal |
| 49 | PPL | Ignition #1 Control |
| 50 |  | Not Used |
| 51 |  | Not Used |
| 52 | PPL/WHT | Ignition #8 Control |
| 53 | RED | Ignition #7 Control |
| 54 | LT BLU/WHT | Ignition #6 Control |
| 55 | DK GRN/WHT | VSS Output Signal |
| 56 | DK GRN | Ignition #5 Control |
| 57 | DK GRN/WHT | Ignition #4 Control |
| 58 | LT BLU | Ignition #3 Control |
| 59 | BRN/WHT | Ignition Control Reference Low Bank 2 |
| 60 | BRN | Ignition Control Reference Low Bank 1 |
| 61 | RED | Transmission Range Signal C |
| 62 | BLK | EGR Pintle Position Ground |
| 63 | BLK | A/C Refrigerant Pressure Sensor Ground |
| 64 |  | Not used |
| 65 |  | Not used |
| 66 |  | Not used |
| 67 |  | Not used |
| 68 |  | Not used |
| 69 |  | Not used |
| 70 |  | Not used |
| 71 | PPL | VSS Signal Low |
| 72 | BLK | PCM Ground |
| 73 |  | Not used |
| 74 |  | Not used |
| 75 | GRY | Left and Right Fuel Tank Sensor Ground |
| 76 | BLK | PCM Ground |
| 77 | PPL | TCC/Brake Switch Signal |
| 78 |  | Not used |
| 79 |  | Not used |
| 80 |  | Not used |

Elmer Boggs	Eboggs_jkvl	1/22/2001

| Circuit Number C2 (Blue) | This table contains all of the Pin connections, Wire colors, and Functions of Connector C2 (Blue). There are 80 pins on this connector |
| --- | --- |

| Pin | Wire Color | Function |
| --- | --- | --- |
| 1 | TAN | HO2S Signal Low Bank 2 Sensor 2 |
| 2 | TAN/WHT | HO2S Signal Low Bank 1 Sensor 2 |
| 3 | TAN | Serial Data (UART) |
| 4 | RED | Camshaft Position Sensor B+ Supply |
| 5 | TAN | HO2S Signal Low Bank 2 Sensor 1 |
| 6 | TAN/WHT | HO2S Signal Low Bank 1 Sensor 1 |
| 7 | RED/BLK | A/C Refrigerant Pressure Sensor Signal |
| 8 | TAN | IAT Sensor Signal |
| 9 | BRN | EGR Pintle Position Sensor Signal |
| 10 | PPL | Fuel Level Sensor Signal |
| 11 |  | Not used |
| 12 | DK BLU | TP Sensor Signal |
| 13 | YEL/BLK | Transmission Fluid Temperature Signal |
| 14 | ORN/BLK | Transmission Fluid Temperature Ground |
| 15 |  | Not used |
| 16 |  | Not used |
| 17 |  | Not used |
| 18 |  | Not used |
| 19 | PNK | PCM Ignition 1 Feed |
| 20 | ORN | PCM Battery Feed |
| 21 | BLK | PCM Ground |
| 22 | YEL/BLK | Crankshaft Position Sensor Ground |
| 23 | BLK | TP sensor Ground |
| 24 | BLK/WHT | Sensor Ground Jumper |
| 25 | BRN | ECT Sensor Ground |
| 26 | ORN/BLK | MAP Sensor Ground |
| 27 |  | Not used |
| 28 | DRK BLU | Engine Cooling Fan Relay #2 and #3 Control |
| 29 |  | Not used |
| 30 | BRN | AIR Pump Relay Control |
| 31 | PPL | AIR Solenoid Relay Control |
| 32 | TAN/BLK | TCC Enable Control |
| 33 | BRN | TCC (PWM) Solenoid Valve Control |
| 34 | GRY | EGR Valve Ground |
| 35 | WHT | Engine Speed 9TACH)) Output Signal |
| 36 | LT BLU/WHT | Transmission Fluid Pressure Control Solenoid Control Low |
| 37 | DK GRN/WHT | Fuel Pump relay Control |
| 38 | LT BLU | EGR Valve Control Circuit |
| 39 | RED/BLK | Transmission Fluid Pressure Control Solenoid Control High |
| 40 |  | Not Used |

Elmer Boggs	Eboggs_jkvl	1/22/2001

Continued on next page

| Circuit Number C2 (Blue) | Table continued. |
| --- | --- |

| Pin | Wire Color | Function |
| --- | --- | --- |
| 41 | PPL | HO2S Signal High Bank 2 Sensor 2 |
| 42 | PPL/WHT | HO2S Signal High Bank 1 Sensor 2 |
| 43 | GRY | TP Sensor 5V Reference |
| 44 |  |  |
| 45 |  |  |
| 46 | PPL | HO2S Signal High Bank 2 Sensor 1 |
| 47 | PPL/WHT | HO2S Signal High Bank 1 Sensor 1 |
| 48 | LT GRN | MAP Sensor Signal |
| 49 | YEL | ECT Sensor Signal |
| 50 |  | Not Used |
| 51 |  | Not Used |
| 52 | DK GRN | Fuel Tank Pressure Sensor Signal |
| 53 |  | Not Used |
| 54 | LT GRN/BLK | IAC Coil B Low |
| 55 | LT BLU/BLK | IAC Coil A Low |
| 56 | LT BLU/WHT | IAC Coil A High |
| 57 | LT GRN/WHT | IAC Coil B High |
| 58 | PPL | Serial Data (Class 2) |
| 59 |  | Not Used |
| 60 | BLK | PCM Ground |
| 61 | ORN | PCM Battery Feed |
| 62 | LT GRN | Crankshaft Position Sensor B+ Supply |
| 63 |  | Not used |
| 64 | GRY | MAP Sensor 5.0 Volt Reference |
| 65 | GRY | 5V Reference |
| 66 | GRY | A/C Refrigerant Pressure Sensor 5.0 Volt Reference |
| 67 | GRY | 5V Reference |
| 68 | LT BLU | Knock Sensor (KS) Rear |
| 69 | DK BLU | Knock Sensor (KS) Front |
| 70 | PNK/BLK | Camshaft Position Sensor ground |
| 71 |  | Not used |
| 72 |  | Not used |
| 73 |  | Not used |
| 74 |  | Not used |
| 75 |  | Not used |
| 76 | BRN | Oil Level Sensor Signal |
| 77 |  | Not used |
| 78 |  | Not used |
| 79 |  | Not used |
| 80 |  | Not used |

Elmer Boggs	Eboggs_jkvl	1/22/2001